## Slide 1: Internet of Things

## Slide 3
CPU
Primary Memory
(RAM)
Secondary Memory
(Hard Disk)
What are the parts of a Basic Computer?
Instruction
Data
Data Address
Input

## Slide 4: What is IoT
A collection of electronic devices designed with built-in internet connectivity, so that they can be monitored, controlled and linked over the Internet via a mobile app or through a laptop or some internet device.
For those Electronic devices designed without built-in internet connectivity, we can extend its capability to have connectivity to the internet either via a cable or through wireless.

## Slide 5: How did this term IoT evolved
Kevin Ashton is known for coining the term "the Internet of Things" to describe a system where the Internet is connected to the physical world via a large number of sensors

## Slide 6: What all devices, can come under IoT ?
Let us discuss

## Slide 7: Is this Microwave Oven a IoT Device?

## Slide 8: Do we get any benefit by making this water pump IoT Enabled?
Let us discuss

## Slide 9: Sensors
What are the different sensors we can think off for IoT?
Write the name of few sensors you can think of

## Slide 10: What else do you need to make a IoT Device
Think

## Slide 11: We need something called actuator to convert electrical signals into action

## Slide 12
How does a computer used for IoT Look like?
CPU
Primary Memory
(RAM)
Secondary Memory
Memory Card (16 GB, 32 GB etc)
Network Interface
12
Electromagnetic
Relay
Electric
Motor
Touch
Screen
LCD (I/O)
Ports
Input

## Slide 13: What is an embedded Computer?
An Electrical system Where Computers are components

## Slide 14: When an embedded Computer is given access to Internet, the whole system becomes an IoT device

## Slide 15
Can you list a few IoT devices you had come across
Let us discuss

## Slide 16: How do we build a device with IoT Enabled
Think

## Slide 17: What are the different components of an End to End IoT solution
What is an end to end Solution?

## Slide 18: End to End IoT solution ?
End to End IoT has four layers
IoT device which has sensors Actuators
Connectivity (Internet)
Processing
Storage.
Internet
IoT device which has sensors Actuators
Processing
Storage

## Slide 19: What benefit do we get out of IoT
IoT is a means for achieving automation through the internet
Jobs which are done manually like:
Data collection from remote equipments
Controlling equipments located at remote locations
Monitoring equipments at remote location
Doing maintenance of equipments at remote locations
Online Tracking and collection of performance data

## Slide 20: Why Internet was Chosen ?
Internet

## Slide 21
What was earlier mode of communication ?
Simple Circuit Switched Telephony could provide reliable Real time Communication
But it came with its own limitations
Microphone
Headset

## Slide 22
Trans Atlantic Cable

## Slide 23
Pros and cons of Circuit Switched
Pros | Cons
The major advantage of circuit switching is that it has a predictable performance that can be guaranteed. Once the circuit has been established, the communication is typically error-free and relatively fast. | The disadvantage of circuit switching is that it requires an initial channel set up that is usually time-consuming
Easy to implement | Needs a dedicated “Connection” between the two points, which gets under utilized when not used.
 | During failure, it is not possible to establish alternative routes. Frequency of failures and down time is very high

## Slide 25: Evolution of Packet switching
Packet switching is a digital networking communications method that groups all transmitted data into suitably sized blocks, called packets, which are transmitted via a medium like copper wire or RF signals .
Since the fault tolerance of Circuit Switched network was very poor, as solution 1950s, American computer scientist Paul Baran developed the concept Distributed Adaptive Message Block Switching which provided a much better fault tolerant system
In a packet switched network, data is transmitted in the form of packet with a “From” and “To” Address, just like a Postal Letter. Such mechanism ensured that a channel is occupied , only during the transmission of the packet, and upon completion of the transmission the channel is made available for the transfer of other traffic[]
Fault Tolerance was given such a importance, so that a packet switched network could withstand a Nuclear Attack

## Slide 27
Advantages of Packet switching
Efficient use of Network with better utilization
Easily get around broken bits or packets.
Packet switching can support high data transmission rates
All the packets not follow same route in Packet Switching, this enables fault tolerance

## Slide 28
Internet
Is a
Packet switched network

## Slide 29
What does this graph indicates ?

## Slide 30: Why there is too much hype about IoT
In future communication is not limited to Human to Human Information exchanges.
It is going to be many folds
Human to Human
Human to Machine
Machine to Human
Machine to Machine
Plants to Machine
Machine to Plants
Plants to Human and back ……
Internet is going to be the medium for all these kind of communication

## Slide 31: What are the IoT platforms.
No | Name | Description
1 | Raspberry Pi | A credit card sized open source computer which runs on linux platform. It uses a ARM Cortex -8 CPU.This board features USB ports for keyboard and mouse, a HDMI port for display and an Ethernet port for wired internet connectivity
2 | Arduino | Arduino is an open-source small computer based on easy-to-use hardware and software, and does not need an Operating system
3 | Beaglebone Black: | low-cost development platform built around ARM Cortex A8 processor. It runs on Linux environment just like the Raspberry Pi.
4 | Intel Edison: | is a tiny computer featuring a Intel Atom CPU and 32 bit Intel Quark microcontroller. This tiny board carries all Wi-Fi and bluetooth modules for connectivity and thus requires no external modules to do so

## Slide 32
No | Software Platform | API exposed for integration | Protocols supported | Type of analytics supported
1 | ThingWorx - MDM IoT Platform | REST API | MQTT, AMQP, XMPP, CoAP, DDS, WebSockets | Predictive analytics(ThingWorx Machine Learning), Real-time analytics (ParStream DB)
2 | IBM IoT Foundation Device Cloud | REST APIand Real TIME API | MQTT, HTTPS | Real-time analytics (IBM IoT Real-Time Insights)
3 | AWS IoT platform | REST API | MQTT, HTTP1.1 | Real-time analytics
4 | Bosch IoT Suite - MDM IoT Platform | REST API | MQTT, CoAP, AMQP,STOMP | No published
5 | Ericsson Device Connection Platform (DCP) - MDM IoT Platform | REST API | CoAP | Not Published

## Slide 33
No | Protocol | Description
1 | MDM | Mobile Device Management
2 | MQTT | Message Queue Telemetry Transport : MQTT is a machine-to-machine (M2M)/"Internet of Things" connectivity protocol.
3 | CoAP | The Constrained Application Protocol (CoAP) is a specialized web transfer protocol for use with constrained nodes and constrained networks in the Internet of Things. The protocol is designed for machine-to-machine (M2M) applications such as smart energy and building automation.”
4 | AMQP | The Advanced Message Queuing Protocol (AMQP) is an open standard application layer protocol for message-oriented middleware.
5 | STOMP | Simple (or Streaming) Text Oriented Message Protocol (STOMP)is a simple text-based protocol, designed for working with message-oriented middleware (MOM). It provides an interoperable wire format that allows STOMP clients
6 | XMPP | Extensible Messaging and Presence Protocol (XMPP) is a communications protocol for message-oriented middleware based on XML (Extensible Markup Language)